## Slide 1: Verification and Validation of the General Mission Analysis Tool (GMAT)
S. Hughes
August 4, 2014
NASA Goddard Space Flight Center

## Slide 2: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 3: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 4: What is GMAT?
GMAT is a general mission design and analysis tool.
Key Applications:
  Mission analysis/optimization
  All orbital regimes
Key characteristics:
open source
high fidelity
feature rich
desktop oriented
Status: Fully tested and flight qualified

## Slide 5: Customizable Tools to Go Anywhere
Customizable trajectory solutions to go anywhere
  LEO
  Libration points
  Lunar
  NEO
  Interplanetary
End-to-End Support
  Design the mission
  Optimize the mission
  Win the proposal
  Fly the mission
Optimal Mars Trajectories
Asteroid (RQ36) Survey
Outer Planet Transfers
Optimal Lunar Flyby
Download and find out more: gmatcentral.org

## Slide 6: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 7: Project Context
2001: Requirements gathering
2002: Architectural design
2003: Implementation of system core
…feature development…
2010: Decision to prepare for operational use
…feature development…
2012–2013: V&V effort
Apr. 2013: First production release (R2013a)
Aug. 2013: Operationally certified (R2013b)

## Slide 8: Goals of the V&V Effort
Technical Goals
  Systematically evaluate and validate all models, components, and functionality
  Fix all critical system defects
  Update working specifications that define system behavior
  Provide high quality end user documentation and training material
  Prepare for system maintenance and further development of a Class B flight qualified system
Strategic goals
  Position GMAT for larger community adoption
  Position GMAT for flight qualification to begin in the spring of 2013.

## Slide 9: V&V Philosophy and Environment
Our Test Environment
Our V&V Philosophy
Test Summary
  Produced about 13000 script tests
  Produced about 3500 GUI tests
Regression Testing
  Script tests run nightly for regression
  GUI tests run weekly

## Slide 10: Component Breakdown
We tested components in logical groups.
GMAT contains many components
  ~30 resources (objects)
  ~25 commands
  System-level components
We divided the testing effort into logical “component areas”
Then, we performed V&V for each component area as a unit
Component Area | Description/Features
Dynamics/Models | Numerical models for orbit and attitude propagation, solar system and coordinate system models including spacecraft orbit state representations, spacecraft ballistic and mass properties, etc.
Powered Flight | Impulsive and finite maneuvering including tanks, thrusters, impulsive maneuver, finite maneuver
Solver Infrastructure | Algorithms and infrastructure for solving boundary value and optimization problems.
Programming Infrastructure | Algorithms and features for customization including custom scripting, user defined variables and arrays, scripted custom equations, built-in astrodynamic computations, control flow, and external interfaces.
Output\Utils | Components to support graphical and data output such as xy-plots, 3-D graphics, report files, and ephemeris files.
Application Control | Inherently interface elements such as file menus, command line interfaces, and the script editor.

## Slide 11: Test Types
Test Type | Description
Numeric | Tests of physical and mathematical models. Numeric tests are performed by comparing output to external "truth".
Functional | Tests that verify non-numeric functionality, such as plotting styles, file formats, and control flow behavior.
Input validation | Tests that ensure user inputs are validated by the system and the correct error messages are provided for invalid user input.
End-to-end | Tests that solve an end-to-end engineering problem such as a lunar transfer or orbital maneuver. These tests are "fit for use" tests and are applications of GMAT to real-world problems.
Stress | Test designed to stress the system and make heavy use of system resources.
Edge/Corner | Tests designed to test models at the boundaries of applicability, in the GMAT context this often means testing models near numerical singularities.
We performed standard test types.
A particular feature can be tested in several ways
  Does it operate correctly on nominal input?
  Does it respond appropriately on invalid input?
  Does it work as a part of the whole system?
We defined 6 test types and applied them to each feature.

## Slide 12: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 13: Dynamics and Modeling
Dynamics and modeling are core to GMAT.
Component area consists of:
  Orbit epoch/state representations
  Spacecraft mass properties
  Attitude representations
  Solar system models
  Numerical integrators
  Force modeling
  Coordinate systems
All went through the full V&V cycle.
Here, we show results for force modeling, integrators, coordinate systems only.
  See the paper for details on the others.

## Slide 14: Orbit Propagation Comparison: Individual Force Modeling
 | Dynamics Model |  |  |  |  |  |  |  | 
Orbital Regime | Spherical Gravity | Harmonic gravity | Tides | Point mass perturbation | SRP | MSISE90 | NRLMSISE00 | Jacchia-Roberts | Relativistic Correction
ISS | 7.1E-06 | 2.5E-03 | 3.3E-01 | 1.5E-05 | 1.3E-01 | 1.8E-01 | 1.1E+00 | 1.9E+00 | 3.8E-02
Sun Sync | 3.9E-05 | 5.0E-04 | 5.7E-01 | 3.6E-05 | 1.7E-01 | 1.8E-02 | 5.8E+00 | 2.0E+00 | x
GPS | 2.7E-06 | 1.5E-04 | 2.5E-02 | 2.3E-05 | 4.7E-02 | 1.4E-05 | 4.2E-06 | 2.7E-06 | x
GEO | 6.3E-06 | 2.8E-05 | 5.0E-02 | 1.8E-04 | 2.4E-05 | 6.3E-06 | 5.2E-05 | 6.3E-06 | 2.3E-03
Molniya | 2.4E-04 | 6.1E-03 | 6.0E+00 | 2.0E-04 | 5.8E-01 | 1.8E-03 | 4.3E+00 | 1.3E-01 | x
Luna | 7.3E-05 | 1.9E-04 | N/A | 2.2E-04 | 1.1E-04 | N/A | N/A | N/A | x
Venus | 9.0E-03 | 1.1E-02 | N/A | 1.4E-02 | 3.7E-02 | N/A | N/A | N/A | x
Mars | 6.1E-02 | 1.2E-01 | N/A | 3.2E-01 | 6.0E-01 | N/A | N/A | N/A | x
Difference between GMAT and reference system for each force model individually
RSS position errors after propagation duration (m)
Most cases show mm- to cm-level agreement.
See paper for initial state vectors, durations, etc.
Velocity errors consistently 2–4 orders of magnitude lower

## Slide 15: Orbit Propagation Comparison: Combined Force Modeling
Test Case | Max Position Diff. RSS (m)
GEO (TBPM,HG,Drag,SRP,Tide) | 9.2227E-01
GEO (TBPM,HG,Drag,SRP) | 1.7184E-04
GPS (TBPM,HG,Drag,SRP,Tide) | 5.2289E-01
GPS (TBPM,HG,Drag,SRP) | 7.5020E-02
ISS (TBPM,HG,Drag,SRP,Tide) | 1.9932E+00
ISS (TBPM,HG,Drag,SRP) | 1.6639E+00
Molniya (TBPM,HG,Drag,SRP) | 5.1301E-01
SunSync (TBPM,HG,Drag,SRP) | 3.3214E-01
Lunar Transfer (TBPM, HG, SRP) | 8.6480E-01
Mars Transfer (TBPM, HG, SRP) | 5.2626E+00
Asteroid (TBPM, HG, SRP) | 4.6731E-03
Earth Moon L2 (TBPM, SRP) | 8.0749E-01
Deep Space (TBPM, Rel) | 3.8275E-02
Titan(TBPM, SRP) | 2.5002E-01
Software | Harm. Gravity | Point Mass | SRP | Drag
GTDS | 0.07 | 0.06 | 2.50 | 575.00
TRACE | 0.0020 | 0.02 | 1.50 | 750.00
Special K | N/A | 0.07 | N/A | N/A
GMAT | 0.01 | 0.0002 | 0.58 | 5.77
GEODYN | N/A | N/A | N/A | 1000
Meter-level or better agreement
for full force modeling.
GMAT compares very well against industry-standard tools.
Worst-case (bounding) comparisons between STK and other tools
Data from Vallado1, with GMAT added
GMAT shows comparable or better worst-case results.

## Slide 16: Numerical Integrators
Orbit | Data | RKV89 | RKN68 | RK56 | PD45 | PD78 | ABM
ISS | Run Time | 1.53 | 1.00 | 2.14 | 2.78 | 1.46 | 3.41
 | Error (m) | 0.003 | 64.060 | 0.022 | 0.002 | 0.006 | 0.012
Molniya | Run Time | 1.32 | 1.47 | 1.99 | 3.08 | 1.00 | 3.35
 | Error (m) | 0.007 | 0.601 | 0.059 | 0.032 | 0.043 | 380.125
Lunar Flyby | Run Time | 1.00 | 1.01 | 2.26 | 2.98 | 2.21 | 3.30
 | Error (m) | 0.063 | 0.017 | 0.002 | 0.023 | 0.000 | 0.236
Mars Transfer | Run Time | 1.02 | 1.04 | 1.14 | 1.40 | 1.00 | 3.07
 | Error (m) | 0.030 | 0.001 | 0.043 | 0.194 | 0.009 | 25.231
Finite burn 1 | Run Time | 1.27 | N/A | 1.24 | 1.26 | 1.00 | 1.45
 | Error (m) | 0.002 | N/A | 0.006 | 0.002 | 0.002 | 0.000
Finite burn 2 | Run Time | 1.03 | N/A | 1.18 | 1.31 | 1.00 | 1.54
 | Error (m) | 0.002 | N/A | 0.000 | 0.000 | 0.001 | 0.003
All integrators were validated. Prince-Dormand 7(8) is the best general-purpose integrator available.
Integrators tested via “closure” tests
  Propagate forward, then backward
  Compare initial and final states
Test performed with and without finite burn
Results shown for both error and performance
Performance results normalized: 1.0 is best-performing result

## Slide 17: Coordinate Systems
Excellent agreement for all transformations
GMAT contains 19 coordinate system types
Conversions from/to each were tested
Shown: Conversion from FK5 (internal system)
  Conversion using circular LEO state vector, SMA = 6800 km
Order-of-magnitude results:
  RSS position: order of mm or better
  RSS velocity: order of μm or better
  Angular: order of 10-8° or better
Conversion Type (FK5 to…) | Position Comparison |  | Velocity Comparison | 
 | RSS Diff (m) | Angle Diff (deg) | RSS Diff (m/s) | Angle Diff (deg)
BodyFixed | 5.79E-03 | 4.88E-08 | 5.65E-06 | 4.23E-08
BodySpinSun | 2.17E-04 | 1.83E-09 | 1.35E-07 | 1.01E-09
GSE | 1.11E-05 | 9.36E-11 | 1.22E-08 | 9.14E-11
GSM | 2.13E-04 | 1.79E-09 | 3.66E-06 | 2.74E-08
ICRF | 7.80E-03 | 6.57E-08 | 1.97E-06 | 1.47E-08
MJ2000Ec | 9.19E-05 | 7.74E-10 | 1.05E-07 | 7.84E-10
MJ2000Eq | 0.00E+00 | 0.00E+00 | 6.39E-12 | 4.78E-14
MODEc | 3.33E-07 | 2.80E-12 | 2.31E-11 | 1.73E-13
MODEq | 9.37E-10 | 7.90E-15 | 6.53E-12 | 4.89E-14
MOEEc | 6.75E-09 | 5.69E-14 | 5.42E-12 | 4.06E-14
MOEEq | 4.90E-09 | 4.13E-14 | 6.14E-12 | 4.59E-14
ObjectReferenced | 1.11E-05 | 9.36E-11 | 1.22E-08 | 9.14E-11
TODEc | 2.00E-04 | 1.69E-09 | 2.20E-07 | 1.65E-09
TODEq | 1.98E-04 | 1.67E-09 | 2.38E-07 | 1.78E-09
TOEEc | 6.55E-05 | 5.52E-10 | 7.20E-08 | 5.39E-10
TOEEq | 2.05E-04 | 1.72E-09 | 2.57E-07 | 1.92E-09
Topocentric | 5.92E-03 | 4.99E-08 | 5.68E-06 | 4.25E-08

## Slide 18: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 19: Output/Utilities Methodology and Results
Extensive & Systematic testing of all components in Output/Utilities feature area was done:
  OrbitView
  Spacecraft Visualization
  GroundTrackPlot
  XYPlot
  ReportFile
  EphemerisFile
  Report
  Toggle On/Off
  ClearPlot
  MarkPoint
  PenUp & PenDown
Only test results for 2-D, 3-D graphics and Ephemeris File are presented

## Slide 20: 2-D Graphics: Ground Track & XY Plot
V&V testing methodology for Ground Track Plot employed standard GMAT GUI testing plans/procedures:
  Testing involved visual inspection of each functional element
  Compared graphical output to expected results from external tools
  Prepared data for automated GUI regression tests that are run
  using the GUI regression test environment
V&V testing methodology for XY Plot:
  Initial testing involved visual inspection of all XY plot functional elements
  Compared XY Plot output with MATLAB as the external benchmark tool
    Equivalent XY data plots generated in MATLAB and GMAT and overlaid
    plots for visual comparison
  For more rigorous & automated GUI testing, test scripts were
  written to test each XY plot element. Test scripts are used by
  the GUI regression test environment

## Slide 21: 3-D Graphics
V&V testing for Orbit View:
  Preliminary testing involved visual inspection of all 3-D graphics behavior
  Key elements of GMAT’s graphics were compared against STK and Celestia benchmarks
GMAT & STK Comparison showing spacecraft trajectory,
ecliptic plane, xy plane and sun-centered MJ2000Eq coordinate sys.
GMAT & Celestia showing star constellations comparison

## Slide 22: Ephemeris File
V&V testing methodology for EphemerisFile:
  Extensive automated testing of ephemeris file component was conducted through GMAT’s script test system
  Test scripts for all functional elements were written
  For CCSDS ephemeris format, we compared interpolation to MATLAB and STK implementations
  For SPK ephemeris format, we tested SPK ephemeris output comparing the results to STK and MICE toolbox

## Slide 23: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 24: Programming Infrastructure
Two testing areas
Script Language: functional testing
  Variables, arrays
  Assignment, mathematics
  Control flow, logical operators
  External interfaces
Mission Data Parameters: numeric testing

## Slide 25: Script Language
All features were tested with all applicable input and output types:
  literals: numeric, strings
  resources: variables, arrays, array elements, string variables, calculated parameters
  mathematical expressions
Special testing for:
  Logical operators: all data types w/ all operators
  MATLAB interface: all data types as input/output
  Mathematical expressions

## Slide 26: Mathematical Expressions
Same syntax as MATLAB expressions
Wrote random generator to generate thousands of valid expressions
Results validated against MATLAB
100 scripts w/ random contents in regression system
Operators | Functions
+ (addition) | sin
- (subtraction) | cos
* (multiplication) | tan
/ (division) | asin
' (transpose) | acos
^ (power) | atan
 | atan2
 | log
 | log10
Example operators and functions

## Slide 27: Mission Data Parameters
Parameters are calculated on request
Can be read-only or read-write
One of three types:
  Standalone
  Central-body dependency
  Coordinate system dependency
Truth sources:
  STK
  custom MATLAB
  custom GMAT scripting
Parameter | Access | Dependency
Spacecraft |  | 
Cartesian position | RW | Coordinate system
Keplerian elements | RW | Coordinate system, celestial body
Epoch | RW | (None)
Attitude quaternion | RW | (None)
Duty cycle | RW | (None)
Thrust scale factor |  | 
Fuel tank |  | 
Fuel mass | RW | (None)
Fuel density |  | 
Impulsive maneuver |  | 
Cartesian maneuver direction | RW | (None)
Example parameters

## Slide 28: Results: Central-Body Parameters
Orbit | Body | Alt. | Beta angle | Orbit energy | Mean motion | Ang. mom. | Vel. at periapsis
GEO | Earth | 5e-12 | < 1e-16 |  | 5e-14 | 8e-12 | 2e-11
 | Venus | 2e-12 | 2e-12 | 8e-11 | 6e-14 | 2e-11 | 4e-11
Hyperbolic | Earth | 3e-9 | 7e-15 | 6e-8 | 2e-11 | 2e-7 | 9e-8
 | Venus | 2e-11 | 3e-14 | 3e-8 | 1e-8 | 2e-8 | 2e-8
Mars | Earth | 2e-12 | < 1e-16 | 3e-9 | 4e-9 | 2e-9 | 2e-9
 | Mars | 4e-8 | < 1e-16 | 2e-9 | 2e-12 | 5e-10 | 5e-10
Luna | Earth | 2e-11 | < 1e-16 | 5e-8 | 3e-14 | 9e-9 | 9e-9
 | Luna | 3e-9 | < 1e-16 | 7e-10 | 6e-13 | 4e-10 | 4e-10
Parameter calculations tested for multiple orbit types, with multiple dependencies
Results compared against STK/Astrogator, custom STK/Astrogator scripting, and custom GMAT scripting
Selection of results shown
Results are percent difference between GMAT and truth solution
  1 = 100% error
  1e-12 = 11 digits of agreement
Excellent agreement for all calculations

## Slide 29: Results: Coordinate-System Parameters
Orbit | Coordinate system | Velocity magnitude | RAAN | Declination | Right ascension of velocity
GEO | Earth J2000 | 4e-12 | 5e-14 | 5e-14 | 2e-9
 | Saturn Fixed | 8e-12 | 2e-5 | 8e-13 | 2e-5
Hyperbolic | Earth J2000 | 3e-8 | 1e-13 | 4e-9 | 4e-9
 | Saturn Fixed | 6e-13 | 2e-6 | 7e-13 | 2e-5
Mars | Mars J2000 | 5e-9 | 2e-11 | 2e-5 | 9e-7
 | Saturn Fixed | 6e-13 | 6e-6 | 3e-13 | 6e-6
Luna | Moon J2000 | 5e-10 | 6e-13 | 2e-6 | 3e-7
 | Saturn Fixed | 4e-13 | 3e-6 | 4e-13 | 2e-5
Parameter calculations tested for multiple orbit types, with multiple coordinate-system dependencies
Results compared against STK/Astrogator
Selection of results shown
Results are percent difference between GMAT and truth solution
  1 = 100% error
  1e-12 = 11 digits of agreement

## Slide 30: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 31: Goals of GUI Testing
Reasonable confidence that GMAT is user-ready
100% coverage of GUI – every widget in the GUI gets exercised at least once
100% requirements fulfillment – every GUI-related requirement is fulfilled by the GUI
Repeatable
Maintainable

## Slide 32: GUI System Tests and “Unit” Tests
Unit tests ensure verification and acceptance testing of every button, menu, text box, etc.
  One unit test project <-> one object (resource, command, script window, mission sequence, etc)
System tests validates the GMAT GUI by testing the entire application
  End-to-end test cases
  Simulating typical end-user interactions
Tests are implemented using SmartBear’s TestComplete GUI testing tool
Test Report History

## Slide 33: GATS and Requirements To Test Matrix
GMAT Automated Test Suite (GATS) tool executes RTTM
  Automate the execution of the GUI tests
  Map tests to requirements
  Report results
~3400 tests executed in 4 days (biweekly)
  Smaller subset executed nightly

## Slide 34: Contents
Introduction to GMAT
Verification and Validation Overview
Dynamics and Modeling
Output and Reporting
Programming Infrastructure
GUI Testing
Conclusions

## Slide 35: Conclusions
Successful system-wide V&V effort led to release of GMAT R2013a, its first production-quality release.
Systematically evaluated and validated all models, components, and functionality
Fixed nearly all critical system defects
Updated working specifications that define system behavior
Provided high quality end user documentation and training material
Prepared for system maintenance and further development of a NASA Class B flight qualified system
Positioned GMAT for larger community adoption
Positioned GMAT for flight qualification
The V&V program enabled a successful follow-on flight qualification effort.

## Slide 36: Backup

## Slide 37: Test Types
Test Type | Description
Numeric Tests | Tests of physical and mathematical models. Numeric tests are performed by comparing output to external "truth".
Functional tests | Tests that verify non-numeric functionality, such as plotting styles, file formats, and control flow behavior.
Input validation | Tests that ensure user inputs are validated by the system and the correct error messages are provided for invalid user input.
End-to-end tests | Tests that solve an end-to-end engineering problem such as a lunar transfer or orbital maneuver. These tests are "fit for use" tests and are applications of GMAT to real-world problems
Stress Tests | Test designed to stress the system and make heavy use of system resources.
Edge corner tests | Tests designed to test models at the boundaries of applicability, in the GMAT context this often means testing models near numerical singularities.
We performed standard test types.
Test Type | Description
Numeric Tests | Tests of physical and mathematical models. Numeric tests are performed by comparing output to external "truth".
Functional tests | Tests that verify non-numeric functionality, such as plotting styles, file formats, and control flow behavior.
Input validation | Tests that ensure user inputs are validated by the system and the correct error messages are provided for invalid user input.
End-to-end tests | Tests that solve an end-to-end engineering problem such as a lunar transfer or orbital maneuver. These tests are "fit for use" tests and are applications of GMAT to real-world problems
Stress Tests | Test designed to stress the system and make heavy use of system resources.
Edge corner tests | Tests designed to test models at the boundaries of applicability, in the GMAT context this often means testing models near numerical singularities.

## Slide 38: Powered Flight

## Slide 39: Example Tank Configuration
Tank | Description | Mass (kg) | Pressure (kPa) | Temp (C) | Ref Temp (C) | Volume (m3) | Fuel Density (kg/m3) | Pressure Model
A | Baseline | 725 | 1200 | 20 | 12 | 0.8 | 1029 | PR
B | High Mass | 820 | 1200 | 20 | 12 | 0.8 | 1029 | PR
C | High Pressure | 725 | 2500 | 20 | 12 | 0.8 | 1029 | PR
D | Low Pressure | 725 | 725 | 20 | 12 | 0.8 | 1029 | PR
E | High Temp | 725 | 1200 | 200 | 12 | 0.8 | 1029 | PR
F | Low Temp | 725 | 1200 | 2 | 12 | 0.8 | 1029 | PR
G | High Ref Temp | 725 | 1200 | 20 | 100 | 0.8 | 1029 | PR
H | Low Ref Temp | 725 | 1200 | 20 | 2 | 0.8 | 1029 | PR
T | High Volume | 725 | 1200 | 20 | 12 | 80 | 1029 | BD
U | Low Density | 725 | 1200 | 20 | 12 | 8.0 | 101.325 | BD
V | High Density | 725 | 1200 | 20 | 12 | 0.8 | 2500 | BD

## Slide 40: Example Thruster Configurations
Coordinate System | Designation | Description
MJ2000Eq | CS0 | J2000-based Earth-centered Earth mean equator inertial
Earth VNB | CS1 | Earth Velocity-Normal-Binormal (VNB) is a non-inertial coordinate system based upon the motion of the spacecraft with respect to the Earth. The X-axis of this coordinate system is along the velocity of the spacecraft with respect to the Earth, the Y-axis is along the instantaneous orbit normal (with respect to the Earth) of the spacecraft, and the Z-axis completes the right-handed set.
Earth LVLH | CS2 | Earth Local Vertical Local Horizontal (LVLH) is a non-inertial coordinate system based upon the motion of the spacecraft with respect to the Earth. The X-axis of this coordinate system is the position of the spacecraft with respect to the Earth, the Z-axis is the instantaneous orbit normal (with respect to the Earth) of the spacecraft, and the Y-axis completes the right-handed set.
SpacecraftBody | CS3 | SpacecraftBody is the attitude system of the spacecraft. Since the thrust is applied in this system, GMAT uses the attitude of the spacecraft, a spacecraft attribute, to determine the inertial thrust direction.
Custom Designed Earth VNB | CS4 | Same coordinate system as Earth VNB. (created using a different user interface)

## Slide 41: Summary of Impulsive Maneuver Results
Orbit | Position RSS Error (m) | Velocity RSS Error (m/s) | Mass Error (g)
Earth | 0 | 0 | 2.27374E-10
Moon | 2.59206E-08 | 0 | 2.27374E-10
Mars | 5.96083E-06 | 1.7764E-12 | 2.27374E-10
Coordinate System | Position RSS Error (m) | Velocity RSS Error (m/s) | Mass Error (g)
Earth Mean Equator J2000 (CS0) | 0 | 0 | 2.27374E-10
Earth VNB (CS1) | 0 | 0 | 2.27374E-10
Earth LVLH (CS2) | 0 | 0 | 2.27374E-10
SpacecraftBody (CS3) | 0 | 0 | 2.27374E-10
Custom Designed Earth VNB (CS4) | 0 | 0 | 2.27374E-10
Test Category | Position RSS Error (m) |  | Velocity RSS Error (m/s) |  | Mass Error (g) | 
 | Low | High | Low | High | Low | High
Orbit | 0 | 6.0e-6 | 0 | 1.8e-12 | 2.3e-10 | 2.3e-10
Maneuver Coordinate System | 0 | 0 | 0 | 0 | 2.3e-10 | 2.3e-10
Tank Configuration | 0 | 0 | 0 | 0 | 0 | 2.3e-10
All | 0 | 6.0e-6 | 0 | 1.8e-12 | 0 | 2.3e-10

## Slide 42: Summary of Finite Maneuver Results
Orbit | Position RSS Error (m) | Velocity RSS Error (m/s) | Mass Error (g)
Earth | 2.644E-03 | 3.415E-06 | 1.547E-05
Jupiter | 2.170E-02 | 1.066E-05 | 2.593E-05
Luna | 1.054E-02 | 3.728E-05 | 8.752E-05
Mars | 1.222E-03 | 1.195E-06 | 2.009E-05
Mercury | 1.129E-03 | 2.450E-06 | 1.097E-05
Neptune | 2.791E-02 | 1.720E-05 | 2.417E-05
Pluto | 5.000E-02 | 7.739E-04 | 1.098E-04
Saturn | 1.877E-03 | 6.404E-07 | 3.369E-06
Uranus | 7.388E-03 | 4.442E-06 | 1.211E-05
Venus | 1.198E-03 | 1.553E-06 | 5.555E-06
Thruster Configuration | Position RSS Error (m) | Velocity RSS Error (m/s) | Mass Error (g)
A | 2.644E-03 | 3.415E-06 | 1.547E-05
B | 1.940E-03 | 2.421E-06 | 1.147E-05
C | 7.279E-04 | 7.070E-07 | 5.189E-07
D | 3.004E-03 | 2.922E-06 | 2.145E-05
E | 5.000E-03 | 6.436E-06 | 2.371E-05
F | 1.135E-03 | 1.080E-06 | 2.938E-07
H | 2.993E-04 | 3.802E-07 | 2.728E-08

## Slide 43: GMAT Test Processes